## Slide 1
Global Warming and Climate change
Unit 6
Social Issues and the Environment
Prepared by; Dr Naresh Kumar Sahoo
Department: Chemistry
Subject: Environmental Studies (CHM1002)
B. Tech (Environmental Studies) 4th and 6th Semester

## Slide 2: Contents
Types, Sources, Level and Production of Green House Gases
Working Principle of Green House Gases
Causes of Climate Change
Introduction of Global Warming and Climate Change
Depletion of Stratospheric Ozone and Climate Change
Global Climate Change Model and Earth energy Budgets
Mitigation of Global Warming
Impact of Global Warming
Notes: 2

## Slide 4
Causes of Climate Change
Feedback Mechanisms
Anthropogenic Global Warming
Bio-thermostat
Variations in Solar Radiation
Solar Irradiance
Sunspot Activity
Earth-Sun Geometry (Milankovitch cycles)
Atmospheric Dust and Volcanoes
Distribution of Continents Plate Tectonics Mountain Building
Ocean Variation
Thermohaline Circulation

## Slide 5
Anthropogenic Global Warming
Principle of Green House Gases ?

## Slide 6: Type and sources Greenhouse Gases
        H2O = 1-3%
        CO2 = .035%
        CH4
        N2O
        O3
        CFC’s
High
Conc.
Trace
Naturally occurring
Anthropogenic
Hydrofluorocarbons (HFCs), perfluorocarbons (PFCs) and sulphur hexafluoride (SF6).
Sources of Green house gases
Sources of ozone

## Slide 7
Photochemical Smog and formation of ground level Ozone

## Slide 11
Depletion of Stratospheric Ozone and Climate change

## Slide 12
Influence amount and pattern of precipitation, Drought
Impact of Global Worming

## Slide 16
Earth energy Budgets

## Slide 17
Recap: Figure 2.8
Neelin, 2011. Climate Change and Climate Modeling, Cambridge UP
7-13 µm
26 W/M2 lost to atmosphere
by convection of water
Condensation of water vapor
Pathways of energy transfer in a global average
26+24+78+40=168
168+67=235
Notes: global.energy.bal.clr.eps from chap2

## Slide 18
Global climate change Model

## Slide 19: Black Body Radiation
Wien’s Law - Peak wavelength emitted by a body
  lpeak (in microns) = 2877/TK
For Sun:
  5780K = temp of photosphere
  lpeak sun = 2877/5780
  = 497 nm
  = 4.97 x 10-7 m
A blackbody is something that emits (or absorbs) electromagnetic radiation with 100% efficiency at all wavelengths.
Blackbody radiation is the radiation emitted at a characteristic wavelength that depends on the body’s absolute temperature.

## Slide 20: Solar Constant
Stephan-Boltzman Law (Energy emitted)
E = sT4
  = Stephan-Boltzman constant = 5.67 x 10-8 Wm-2K-4
E is proportional to the area under the Planck function curve
Esun = 6.3 x 107 W/m2
Only a small fraction of sun’s energy is received by the Earth

## Slide 21: Earth
Incoming radiation is short wave.
Outgoing radiation is long wave.
If the Earth is a blackbody at steady state
  Incoming = outgoing
  Energyin = Energyout

## Slide 22: Earth- Incoming Radiation
Solar radiation intersects Earth as a disk (pr2)
Energyin = Energyin from sun (S) – Reflected Solar Energy
  = pr2 S - pr2 Sa
  Where:
  r = radius of Earth (6360 km)
  S = solar constant (1368 W/m2)
  = albedo (earth’s reflectivity) (~30%)
  = pr2 S (1- a)

## Slide 23: Earth- Outgoing Radiation
Earth radiates as a sphere with area 4pr2 (m2)
Stephan-Boltzmann equations defines outgoing energy based on radiating temperature
Energyout = 4pr2 sTe4
  (units (m2)(Wm-2K-4)(K4) = W
  Total energy emitted by the Earth

## Slide 24: Earth’s Radiation Budget
If the earth were a black body the in = out
Set incoming = outgoing
  pr2 S (1- a) = 4pr2 sTe4
  Simplify:
  S/4 (1- a) = sTe4
  Solve for Te
  Te = 255K (-18 °C)

## Slide 25: Earth as a Black Body
Earth’s actual surface temperature
  Ts = 288K (15°C)
  lpeak (mm) = 2877/288 = 10 mm (IR)
  Ts - Te = 288 – 255 = 33
  = Earth’s natural greenhouse
Interactions within atmosphere alter radiation budget (Earth is not a black body)
Greenhouse Effect

## Slide 26: Mitigation of Global Warming
Conservation
  Reduce energy needs
  Recycling
Alternate energy sources
  Nuclear
  Wind
  Geothermal
  Hydroelectric
  Solar
  Fusion?
Notes: Methods of mitigating global warming include 
  Conservation 
    Reduce energy needs, such as electrical usage, petroleum usage, reduced packaging 
    Recycling, which uses less energy to produce products compared to 
  Another way to reduce carbon emissions is to use alternate energy sources, such as 
    Nuclear 
    Wind 
    Geothermal 
    Hydroelectric 
    Solar 
    Fusion? 

## Slide 28: Storage of CO2 in Geological Formations
Depleted oil and gas reservoirs
CO2 in enhanced oil and gas recovery
CO2 in enhanced coal bed methane recovery
Adapted from IPCC SRCCS Figure TS-7
3a
2
3b
1
4
Notes: Another promising way to reduce global warming is to store carbon dioxide underground.  Carbon dioxide can be pumped into depleted oil and gas reservoirs.  In addition, carbon dioxide can be pumped into existing oil and gas deposits to enhance recovery. Another method  Carbon dioxide can also be used to enhance methane recovery from coal beds. 